## Slide 1: Icelandic ID-cards: ICAO Digital Barcodes (IDB)
18 January 2024

## Slide 2: Icelandic ID-card: Small CAN barcode on card front
Identifier+flag:
Header:
Message Zone:
Payload structure to be encoded
Base32 and de-padding:
Barcode from Base32 (6x6mm 600dpi):
Barcode ID (4)
"IDB1"
Barcode flag (1)
“C“
Country (2)
C40 ("ISL")
Msg.Type (1)
0x09
CAN value (4)
C40 (Card Access Number)
MSG Zone (4) C40(CAN)
IDB1(4chars)
Encoded Payload (∼16 characters)
len(1) 4
Header (2)
C40 ("ISL")
Msg.Type (1)
0x09
len(1) 4
Msg zone tag(1)
0x61
Msg zone tag(1)
0x61
len(1) 4
len(1) 4
Encoded Payload (∼16 characters)

## Slide 3: Icelandic ID-card: Large barcode on card reverse
Front:
Header:
MRZ message:
Signature zone:
Barcode ID (4)
"IDB1"
Barcode flag (1)
"D"
Country (2)
("ISL")(c40)
Signature alg(1)
0x01, 0x02 or 0x03
Certificate ref (5)
(sha1 end)
Sign.date (4)
Date (encoded)
MRZ (90)
C40 ("IDISLIS1234567X121212 1239 121212XF291011XISL 3 AEVARSDOTTIR THURIDUR OESP ")
Full name (1-44)
"Þuríður Ösp Ævarsdóttir"
Tiny Facial (<1024)
Jpeg2000 (B/W+shrink+compress)
Signature Tag (1)
0x7F
Signature (<73)
(DER encoded – Signature on Header+All Messages)
MRZ tag (1)
0x07
Msg len(3) DER-TLV
Msg zone tag(1)
0x61 ("T")
Nat.MsgType (1)
0xAA
len(1) 1-44
Nat.MsgType (1)
0xAB
len(3) DER-TLV
len(1) <73
MRZ len(1) 0x3C (60) or 0x5A (90)

## Slide 4: Final encoding of large barcode
Encoded structure for signing (<1129):
Signed structure (<1204):
ZLIB compressed level9 (∼1196 hex bytes):
Base32 encoded (8/5) +de-padding (<1866 chars):
Barcode from Base32:
Header (16)
MRZ message (63)
FullName message (47)
TinyFacial message (<1005)
Signature zone (<75)
Header (16)
MRZ message (63)
FullName message (47)
TinyFacial message (<1005)
Signature zone
Header
MRZ message
FullName message
TinyFacial message
Signature zone (<120)
Header (16)
MRZ message (69)
FullName message (53)
TinyFacial message (<1608)